## Slide 1: Machine Learning For Transport and Mixing Processes
CIEG 678 Ryan Schanta
Ye et al. 2021

## Slide 2: Overview
Review of PINNs
PINNs for RANS Closure Problems
  Automatic Differentiation
Demo: Building a PINN
  Problem Formulation
  Coding Strategy
  Analysis & Adapting to Results
Summary

## Slide 3: Recap: PINNS
Standard “Data Science” Metrics
Goal of ML model: minimize loss term
Challenges
  Overfitting
  Insufficient Data
  Generalizability
Physics Informed Neural Network
Leverages information about problem
Choose to enforce:
  Governing PDES
    Navier Stokes
    Conservation of Mass
    Known Parametrizations
  Boundary Conditions
  Initial Conditions
  RMSE/Data (if known)
Comparatively expensive
Domain knowledge required

## Slide 4: PINNS in RANS
Concept: provides another constraint!
RANS 2-equation model
Relies on empirical coefficients
Goal: Can we tune the parameters with DNS data to get better coefficients for certain geometries?
Implications: Efficient use of physical constraints and available data
From S. Luo et al (2020)

## Slide 5: PINNS in RANS
Feedforward Neural Network for and
Differentiate
Outputs
Plug into equation
Minimize Loss
From S. Luo et al (2020)

## Slide 6: PINNS in RANS
Feedforward Neural Network for and
Differentiate
Outputs
Plug into equation
Minimize Loss
Recall: Networks have learnable weights and biases
Input Parameters
Bias
Activation function
Hyperparameters/Design Choices
  Number of Layers
  Activation Function
  Batching strategy
From S. Luo et al (2020)

## Slide 7: PINNS in RANS
Feedforward Neural Network for and
Differentiate
Outputs
Plug into equation
Minimize Loss
Derivatives of outputs needed
Typical methods cost prohibitive
  Finite differences
  Symbolic math
Automatic Differentiation- elegant solution
  Computer arithmetic and data structures
  Concept: Everything is chain-rulable!
From S. Luo et al (2020)

## Slide 9: PINNS in RANS
Feedforward Neural Network for and
Differentiate
Outputs
Plug into equation
Minimize Loss
Auto-differentiate and plug into RANS equations
Calculate Loss
  Both DNS and Physics!
Iteratively adjust!
From S. Luo et al (2020)

## Slide 10: PINNS in RANS: Results
Prediction of Flow Separation
  Classically difficult case
PINN-calibrated RANS: 22% improvement
  Doesn’t completely get it
Takeaways
Middle-ground
Still RANS at the end of the day
Used to improve existing methodologies, not replace them!
Standard RANS
PINN Enhanced RANS
DNS
Comparison of the time averaged turbulent kinetic energy
From S. Luo et al (2020)
Original |  |  |  |  | 
PINN |  |  |  |  | 
Original |  |  |  |  | 
PINN |  |  |  |  | 

## Slide 11: Building a PINN from Scratch
Example 1.4: 1D Diffusion Problem
  Assume some initial distribution
    Gaussian spike
    Triangular spike

## Slide 12: Building Blocks
Neural Network Architecture
Loss Function with Conditions to Enforce
PDE Condition
Boundary Condition
Initial Condition
Relative weight factors for IC/BC/PDE losses
How many layers?
How many nodes per layer?
Which activation functions?
Dropout? Convolution? Other operations?

## Slide 13: Code Process
1. Define some neural network that takes in 2 inputs and ends up with 1 output
2. Set up a loop to repeatedly run through network and update weights
2a. Set up a gradient tape on the trainable variables for gradient descent
2b. Set up a gradient tape on the output parameters for auto-differentiating boundary conditions
2c. Calculate your loss from PDE, IC, and BC weighting
2d. Perform gradient descent* to march the loop forward
3. Repeat until convergence
More involved than a standard Keras/TF network
  Need to go “under the hood” for Loss Function
Several libraries have since been developed
  Most use some version of gradient tape
Not yet a fully “standardized” workflow in any domain!
*Many optimization algorithms are available! I used Adam

## Slide 15: Parameter Hyperparameter Choices
4 Layers
64 Nodes each layer
250 epochs
Kept Constant
Tried and
Ignored for now
Tried and activation functions
Gaussian Bump and Triangular Bump Initial Distributions

## Slide 16
Activation Function

## Slide 17
Activation Function

## Slide 20: Summary and Next Steps
PINNs provide new opportunities for solving differential equations
Caution must be applied
  “Informed” > Good judgment
Sensitivity:
  Machine Learning Hyperparameters
  Physical Parameters
“Physically-inspired” networks
From Wikipedia: https://en.wikipedia.org/wiki/Physics-informed_neural_networks
Luo, Shirui, Madhu Vellakal, Seid Koric, Volodymyr Kindratenko, and Jiahuan Cui. “Parameter Identification of RANS Turbulence Model Using Physics-Embedded Neural Network.” In High Performance Computing, edited by Heike Jagode, Hartwig Anzt, Guido Juckeland, and Hatem Ltaief, 12321:137–49. Lecture Notes in Computer Science. Cham: Springer International Publishing, 2020. https://doi.org/10.1007/978-3-030-59851-8_9.
Citation for Luo paper